GMP Products
Anionic surfactants
Alkyl benzene sulphonates: base surfactant in liquid and powder household detergents, acid cleaners, hand cleaners
Alcohol sulphates: high foaming liquid shampoos, toiletries and bubble baths
Alcohol ethoxy sulphates: high foaming liquid shampoos, toiletries and bubble baths
Non-ionic surfactants
Detergent alcohols: base material for preparation of alcohol ethoxylates, sulphates and ethoxy sulphates
Linear alkyl benzene: base material for LABSA, specialty solvent
Detergent alcohol ethoxylates: wetting agents with moderate foam for industrial and household cleaners, base material for preparation of alcohol ethoxysulphates
Specialty surfactants
Detergent concentrate: concentrate base for household and industrial detergents
[Speaker Notes: ‹#›]

---
Sulphurex Process Plant
Air drying (Unit 11)
Sulphur melting, burning & SO2/SO3 conversion (Unit 12)
Sulphonation/Sulphation (Unit 16)
Neutralization (Unit 17)
Exhaust Gas Cleaning (Unit 14)
Tank Farm (Unit 19)

---
Air Drying
H2O(l)
H2O(g)
condensation
NaSiO2.9H2O
NaSiO2
9 H2O
+
adsorption
H2SO4
SO3
H2O
Moisture in the process air reacts with SO3 to produce sulphuric acid and oleum, resulting in poor product quality and plant corrosion.

---
Sulphur melting, burning and SO2/SO3 conversion
Optimal catalysis temperature 440 oC
Exothermic
Three stage converter tower with interstage cooling
GMP achieves 98% conversion
S(l)
S(s)
150 oC
SO2
Sulphur dioxide
S
Sulphur
O2
Oxygen
ΔH = -292 kJ/mol
Very exothermic
Furnace outlet temperature 650 oC
SO3
Sulphur trioxide
SO2
Sulphur dioxide
½O2
Oxygen
ΔH = -97 kJ/mol
V2O5

---
Sulphonation/Sulphation
Fast Reaction:
Rapid and even mixing of feedstock and gas
Tight control of mole ratio
Excellent temperature control
Multitube falling film reactor, residence time 2 minutes
Slow reaction (Ageing):
Plug flow
Temperature control
About 40 minutes
Hydrolysation
High shear mixing
Temperature control

---
Sulphonation
Exothermic
A 2-step reaction with competing reactions
Finished product contains several components
R-C6H5
LAB
SO3
Sulphur trioxide
R-C6H4-SO3-H
Sulphonic acid
ΔH = -170 kJ/mol

---
Sulphation
Also a complex reaction
Resultant acid is unstable and requires immediate neutralization, generally with ammonia or caustic
R-OH
Alcohol or
Alcohol ethoxylate
SO3
Sulphur trioxide
R-OH-SO3-H
Alkyl hydrogen sulphate
ΔH = -150 kJ/mol

---
Neutralization
NaOH
Sodium hydroxide
R-OH-SO3-Na
Sodium alkyl sulphate
R-OH-SO3-H
Alkyl hydrogen sulphate
H2O
NH3
Ammonia
R-OH-SO3-NH4
Ammonium alkyl sulphate
ΔH = -120 kJ/mol
R-OH-SO3-H
Alkyl hydrogen sulphate

---
Exhaust Gas Cleaning
Caustic Scrubbing
Removes unconverted SO2
Virtually no SOx emissions to atmosphere
10% sodium sulphite/sulphate scrubber effluent used in powder manufacture at UL Petone.
2 NaOH
Sodium hydroxide
Na2SO3
Sodium sulphite
SO2
Sulphur dioxide
H2O
2 NaOH
Sodium hydroxide
Na2SO4
Sodium sulphate
SO3
Sulphur trioxide
H2O
Electrostatic Precipitation
Removes organic carryover to prevent foaming in scrubber
Mostly removes unreacted SO3
H2O
H2SO4
Sulphuric acid
SO3
Sulphur trioxide

---
Quality Control
Raw Materials: Every delivery
In process: Every 2 hours
IN PROCESS
Appearance	(visual)
pH	(pH meter)
Moisture	(titration)
Colour	(absorbance)
Direct acidity	(titration)
UOM	(chromatography)
Finished Product: Every batch or tank
Scrubber Discharge
SCRUBBER DISCHARGE
pH	(pH meter)
Sulphate	(titration)
Sulphite	(SO3 strip)
RAW MATERIALS
Appearance	(visual)
pH	(pH meter)
Moisture	(titration)
Colour	(colour wheel)
Density	(density meter)
FINISHED PRODUCT
Appearance	(visual)
pH	(pH meter)
Moisture	(titration)
Colour	(absorbance)
UOM	(chromatography)
Active matter(titration)
Sulphate	(titration)
Dioxane	(chromatography)

---
Waste Management
SO2/SO3 EMISSIONS
Minimal , well within RMA consent
ESP WASTE
~5MT/annum for 3rd party disposal (SLES production)
~20MT/annum reprocessed (LABSA production)
SULPHATE LIQUOR
~10% sodium sulphate
~1400MT/annum
Delivered for reprocessing or
Discharged to trade waste with water dilution, within Trade Waste limits
WASHWATER
Unit 17 washings reprocessed
Other washings discharged within Trade Waste limits